## Slide 1: Ce que nous allons voir aujourd’hui
Chemin de données
P&H : 4.1, 4.3-4.8

## Slide 2
adresse | Instruction
. . . 0xf408 0xf409 0xf40A . . . | . . . add r2 , r5, M[0xa4] jpz 0xf400 lw r0, M[0xAF] . . .
adresse | Instruction
. . . 0xf408 0xf409 0xf40A . . . | . . . add r2 , r5, M[0xa4] jpz 0xf400 lw r0, M[0xAF] . . .
Contrôleur Mémoire
BUS de commandes
BUS de données
BUS d’adresses
Décodeur
Instruction
Commandes
de BUS
1
b1
17
01
23
00
c2
45
00
PC
MAR
0xf408
IR
MDR
r2 , r5
a4
add
45
17
ALU
5C
P
LIRE
ECRIRE
0xf408
0xf409
ACC
FLAGS
C-BUS
CU
REGISTRES
0x95a4
add
Contenu de la mémoire
Notes: rappel

## Slide 3: Implémentation d’instructions MIPS
Exemple d’implémentation des instructions MIPS suivantes :
  Arithmétique : add addi sub and or slt
  Transfert de données : lw sw
  Branchement : beq
Nous allons concevoir une implémentation en cycle unique. C.-à-d. Le temps d’exécution de chacune de nos instructions est FIXE et le même pour tous.
Ex : si l’instruction add mets 8 nanosecondes (ns) pour s’exécuter (notre cycle) alors cela va de soit avec “addi”, “sub”, …
Notes: 1. Fetch the instruction The next instruction is fetched from the memory address that is currently stored in the Program Counter (IAR), and stored in the Instruction register (IR). At the end of the fetch operation, the PC points to the next instruction that will be read at the next cycle.
2. Decode the instruction The decoder interprets the instruction. During this cycle the instruction inside the IR (instruction register) gets decoded.
3. Execute The Control Unit of CPU passes the decoded information as a sequence of control signals to the relevant function units of the CPU to perform the actions required by the instruction such as reading values from registers, passing them to the ALU to perform mathematical or logic functions on them, and writing the result back to a register. If the ALU is involved, it sends a condition signal back to the CU.
4. Store result The result generated by the operation is stored in the main memory, or sent to an output device. Based on the condition of any feedback from the ALU, Program Counter may be updated to a different address from which the next instruction will be fetched.

## Slide 4: Unités de « Mémoire »
Read address
Instruction [31-0]
Instruction
memory
Read address
Read data
Data
memory
Write address
Write data
MemWrite
MemRead
Architecture Harvard (mémoire distinctes pour les instructions et les données)
Ces mémoires sont 32-bits de large (bus de donnée de 32 bits) afin qu’on puisse lire les instructions et/ou les mots de donnée en une seule opération.
Les lignes bordeaux représentent les signaux de contrôle. MemRead et MemWrite sont mis à « 1 » si l’unité « Data memory » doit être lue ou écrite respectivement, ils sont toujours à « 0 » autrement.
Pour maintenant, on suppose qu’on ne peut pas écrire dans l’unité « Instruction memory ». On va prétendre que le programme est déjà présent et ne change pas au cours de son exécution.

## Slide 5: Récupération d’instructions « fetching »
Le processeur est dans une boucle infinie. Il récupère des instructions de la mémoire et les exécute.
Le registre « Program Counter (PC) » ou « Compteur Ordinal » en français contient l'adresse de l'instruction en cours.
Les instructions du MIPS R3000 ont toutes une taille de 32 bits (C.-à-d. quatre octets). Le registre PC doit donc être incrémenter de « 4 » pour lire la prochaine instruction dans l’ordre.
Read address
Instruction [31-0]
Instruction
memory
Add
P
C
4

## Slide 6: Unités « UAL » et « Banc de registres »
Toute instruction régulière (R-type) DOIT accéder aux Registres et à l’Unité Arithmétique et Logique (UAL).
Le « Banc de Registres » du MIPS R3000 contient 32 registres, donc cinq bits suffisent pour spécifier un registre donné.
On peut LIRE deux registres en MÊME temps.
RegWrite est mis à « 1 » si un registre doit être modifié.
Voici une simple UAL avec cinq opérations, sélectionnées par un signal de contrôle sur trois bits (ALUOp).
UAL
ALUOp
ALUOp | Fonction
000 001 010 110 111 | and or add sub slt
Read
register 1
Read data 1
Registers
Read
register 2
Write
register
RegWrite
Write
data
5
5
5
Read data 2

## Slide 7: Format d’instructions « R – type »
Exemples :
add $18, $8, $17 # $18 := $8 + $17
and $12, $10, $11 # $12 := $10 and $11
 | 000000 | 01000 | 10001 | 10010 | 00000 | 100000
 | 000000 | 01010 | 01011 | 01100 | 00000 | 100100
 | 31 26 | 25 21 | 20 16 | 15 11 | 10 6 | 5 0
R – type (Regular) : | opcode | rs | rt | rd | sh | func
Opérations « registre – registre »
Manipulation de trois registres (opérations arithmétiques et logiques)
Notes: rappel

## Slide 8
Read
register 1
Read data 1
Registers
Read
register 2
Write
register
RegWrite
Write
data
Read data 2
UAL
ALUOp
I[15-11]
I[25-21]
I[20-16]
 | 31 26 | 25 21 | 20 16 | 15 11 | 10 6 | 5 0
R – type | opcode | rs | rt | rd | sh | func
Read address
Instruction [31-0]
Instruction
memory
Add
P
C
4

## Slide 9: Format d’instructions « I – type »
Exemples :
sw $a0, 16($sp) # mem4[16 + ($sp)] := $a0
addi $11, $10, -4 # $11 := $10 - 4
 | 101011 | 11101 | 00100 | 0000 0000 0001 0000
 | 001000 | 01010 | 01011 | 1111 1111 1111 1100
 | 31 26 | 25 21 | 20 16 | 15 |  | 0
I – type (Immediate) : | opcode | rs | rt | Valeur immédiate |  | 
Opérations « registre – immédiat »
Manipulation de constantes, transfert d’informations, branchements conditionnels
0000 0000 0000 0000 1111 1111 1111 11002 = 6553210
1111 1111 1111 1111 1111 1111 1111 11002 = -410
0000 0000 0000 0000 0000 0000 0001 00002 = 1610

## Slide 10
Read
register 1
Read data 1
Registers
Read
register 2
Write
register
RegWrite
Write
data
Read data 2
UAL
ALUOp
I[15-11]
I[25-21]
I[20-16]
 | 31 26 | 25 21 | 20 16 | 15 11 | 10 6 | 5 0
R – type | opcode | rs | rt | rd | sh | func
Read address
Instruction [31-0]
Instruction
memory
Add
P
C
4

## Slide 11
Read
register 1
Read data 1
Registers
Read
register 2
Write
register
RegWrite
Write
data
Read data 2
UAL
ALUOp
I[15-11]
I[20-16]
Read address
Instruction [31-0]
Instruction
memory
 | 31 26 | 25 21 | 20 16 | 15 11 | 10 6 | 5 0
R – type | opcode | rs | rt | rd | sh | func
addi | 001000 | rs | rt | Valeur immédiate |  | 
0mux1
RegDst
sign
extend
1mux0
ALUSrc
I[25-21]
Add
P
C
4
I[15-0]

## Slide 12
Read
register 1
Read data 1
Registers
Read
register 2
Write
register
RegWrite
Write
data
Read data 2
UAL
ALUOp
I[15-11]
I[25-21]
I[20-16]
Read address
Instruction [31-0]
Instruction
memory
0mux1
RegDst
sign
extend
 | 31 26 | 25 21 | 20 16 | 15 11 | 10 6 | 5 0
R – type | opcode | rs | rt | rd | sh | func
addi | 001000 | rs | rt | Valeur immédiate |  | 
lw | 100011 | rs | rt | Valeur immédiate |  | 
Read address
Read data
Data
memory
MemRead
MemToReg
1mux0
1mux0
ALUSrc
Add
P
C
4
I[15-0]

## Slide 13
Read
register 1
Read data 1
Registers
Read
register 2
Write
register
RegWrite
Write
data
Read data 2
UAL
ALUOp
I[15-11]
I[20-16]
Read address
Instruction [31-0]
Instruction
memory
0mux1
RegDst
sign
extend
 | 31 26 | 25 21 | 20 16 | 15 11 | 10 6 | 5 0
R – type | opcode | rs | rt | rd | sh | func
addi | 001000 | rs | rt | Valeur immédiate |  | 
lw / sw | 10X011 | rs | rt | Valeur immédiate |  | 
Read address
Read data
Data
memory
Write address
Write data
MemWrite
MemRead
MemToReg
1mux0
1mux0
ALUSrc
I[25-21]
Add
P
C
4
I[15-0]

## Slide 14
Read
register 1
Read data 1
Registers
Read
register 2
Write
register
RegWrite
Write
data
Read data 2
UAL
ALUOp
I[15-11]
I[25-21]
I[20-16]
Read address
Instruction [31-0]
Instruction
memory
0mux1
RegDst
sign
extend
Read address
Read data
Data
memory
Write address
Write data
MemWrite
MemRead
MemToReg
1mux0
1mux0
ALUSrc
 | 31 26 | 25 21 | 20 16 | 15 0
beq | 000100 | rs | rt | offset
 | if ( ($rs) == ($rt) ) PC = PC + 4 + ( offset << 2 ) |  |  | 
?
Add
P
C
4
I[15-0]

## Slide 15
Read
register 1
Read data 1
Registers
Read
register 2
Write
register
RegWrite
Write
data
Read data 2
UAL
ALUOp
I[15-11]
I[25-21]
I[20-16]
Read address
Instruction [31-0]
Instruction
memory
Add
P
C
4
0mux1
RegDst
sign
extend
Read address
Read data
Data
memory
Write address
Write data
MemWrite
MemRead
MemToReg
1mux0
1mux0
ALUSrc
Add
<< 2
0mux1
PCSrc
zero
 | 31 26 | 25 21 | 20 16 | 15 0
beq | 000100 | rs | rt | offset
+
I[15-0]

## Slide 16: Chemin des instructions régulières (R-type)
PCSrc
Read
register 1
Read data 1
Registers
Read
register 2
Write
register
RegWrite
Write
data
Read data 2
UAL
ALUOp
I[15-11]
I[25-21]
I[20-16]
Read address
Instruction [31-0]
Instruction
memory
Add
P
C
4
0mux1
RegDst
sign
extend
Read address
Read data
Data
memory
Write address
Write data
MemWrite
MemRead
MemToReg
1mux0
1mux0
ALUSrc
Add
<< 2
0mux1
I[15-0]
zero

## Slide 17: Chemin de l’instruction « addi »
PCSrc
Read
register 1
Read data 1
Registers
Read
register 2
Write
register
RegWrite
Write
data
Read data 2
UAL
ALUOp
I[15-11]
I[25-21]
I[20-16]
Read address
Instruction [31-0]
Instruction
memory
Add
P
C
4
0mux1
RegDst
sign
extend
Read address
Read data
Data
memory
Write address
Write data
MemWrite
MemRead
MemToReg
1mux0
1mux0
ALUSrc
Add
<< 2
0mux1
I[15-0]
zero

## Slide 18: Chemin de l’instruction « lw »
PCSrc
Read
register 1
Read data 1
Registers
Read
register 2
Write
register
RegWrite
Write
data
Read data 2
UAL
ALUOp
I[15-11]
I[25-21]
I[20-16]
Read address
Instruction [31-0]
Instruction
memory
Add
P
C
4
0mux1
RegDst
sign
extend
Read address
Read data
Data
memory
Write address
Write data
MemWrite
MemRead
MemToReg
1mux0
1mux0
ALUSrc
Add
<< 2
0mux1
I[15-0]
zero

## Slide 19: Chemin de l’instruction « sw »
PCSrc
Read
register 1
Read data 1
Registers
Read
register 2
Write
register
RegWrite
Write
data
Read data 2
UAL
ALUOp
I[15-11]
I[25-21]
I[20-16]
Read address
Instruction [31-0]
Instruction
memory
Add
P
C
4
0mux1
RegDst
sign
extend
Read address
Read data
Data
memory
Write address
Write data
MemWrite
MemRead
MemToReg
1mux0
1mux0
ALUSrc
Add
<< 2
0mux1
I[15-0]
zero

## Slide 20: Chemin de l’instruction « beq » cas $rs != $rt
PCSrc
Read
register 1
Read data 1
Registers
Read
register 2
Write
register
RegWrite
Write
data
Read data 2
UAL
ALUOp
I[15-11]
I[25-21]
I[20-16]
Read address
Instruction [31-0]
Instruction
memory
Add
P
C
4
0mux1
RegDst
sign
extend
Read address
Read data
Data
memory
Write address
Write data
MemWrite
MemRead
MemToReg
1mux0
1mux0
ALUSrc
Add
<< 2
0mux1
I[15-0]
zero

## Slide 21: Chemin de l’instruction « beq » cas $rs == $rt
PCSrc
Read
register 1
Read data 1
Registers
Read
register 2
Write
register
RegWrite
Write
data
Read data 2
UAL
ALUOp
I[15-11]
I[25-21]
I[20-16]
Read address
Instruction [31-0]
Instruction
memory
Add
P
C
4
0mux1
RegDst
sign
extend
Read address
Read data
Data
memory
Write address
Write data
MemWrite
MemRead
MemToReg
1mux0
1mux0
ALUSrc
Add
<< 2
0mux1
I[15-0]
zero

## Slide 22: Signaux de contrôle et de commande
Read
register 1
Read data 1
Registers
Read
register 2
Write
register
RegWrite
Write
data
Read data 2
UAL
ALUOp
I[15-11]
I[25-21]
I[20-16]
Read address
Instruction [31-0]
Instruction
memory
Add
P
C
4
0mux1
RegDst
sign
extend
Read address
Read data
Data
memory
Write address
Write data
MemWrite
MemRead
MemToReg
1mux0
1mux0
ALUSrc
Add
<< 2
0mux1
PCSrc
zero
I[15-0]
Notes: Chemin de l’instruction est dirigé par des lignes de contrôle et de commande

## Slide 23: Signaux de contrôle et de commande
sw et beq sont les seules instructions dans notre exemple d’instructions qui ne modifient pas le contenu des registres.
Seules les instructions lw, sw et addi utilisent le champ « immédiat ».
ALUOp est fonction du champs « func » pour les instructions régulières (R-type).
Le signal de contrôle PCSrc (non listé ici) est mis à « 1 » si l’instruction exécutée est beq ET si le flag « zero » de l’unité Arithmétique et Logique est « vrai ».
Instruction | RegDst | RegWrite | ALUSrc | ALUOp | MemWrite | MemRead | MemToReg
add | 1 | 1 | 1 | 010 | 0 | 0 | 0
sub | 1 | 1 | 1 | 110 | 0 | 0 | 0
and | 1 | 1 | 1 | 000 | 0 | 0 | 0
or | 1 | 1 | 1 | 001 | 0 | 0 | 0
slt | 1 | 1 | 1 | 111 | 0 | 0 | 0
addi | 1 | 1 | 0 | 010 | 0 | 0 | 0
lw | 0 | 1 | 0 | 010 | 0 | 1 | 1
sw | X | 0 | 0 | 010 | 1 | 0 | X
beq | X | 0 | 1 | 110 | 0 | 0 | X

## Slide 24: Génération des signaux de contrôle
RegDst
RegWrite
ALUSrc
MemWrite
MemRead
MemToReg
ALUOp
isBEQ
Décodeur
d’instructions
Read address
Instruction [31-0]
Instruction
memory
I[31-26]
I[5-0]
Func
Opcode
3
zero
UAL
PCSrc

## Slide 25: Etapes d’exécution d’une instruction MIPS
Read
register 1
Read data 1
Registers
Read
register 2
Write
register
RegWrite
Write
data
Read data 2
UAL
ALUOp
I[15-11]
I[25-21]
I[20-16]
Read address
Instruction [31-0]
Instruction
memory
0mux1
RegDst
sign
extend
Read address
Read data
Data
memory
Write address
Write data
MemWrite
MemRead
MemToReg
1mux0
1mux0
ALUSrc
I[15-0]
Exemple pour l’instruction « lw » ( par soucis de clarté, on va ignorer dans cet exemple le bloc de circuit lié à l’incrémentation du registre « PC » ).
Notes: Chemin de l’instruction est dirigé par des lignes de contrôle et de commande

## Slide 26: Etapes d’exécution d’une instruction MIPS
Read
register 1
Read data 1
Registers
Read
register 2
Write
register
RegWrite
Write
data
Read data 2
UAL
ALUOp
I[15-11]
I[25-21]
I[20-16]
Read address
Instruction [31-0]
Instruction
memory
0mux1
RegDst
sign
extend
Read address
Read data
Data
memory
Write address
Write data
MemWrite
MemRead
MemToReg
1mux0
1mux0
ALUSrc
I[15-0]
Recherche de l’instruction ( Instruction Fetch – IF )
Notes: Chemin de l’instruction est dirigé par des lignes de contrôle et de commande

## Slide 27: Etapes d’exécution d’une instruction MIPS
Read
register 1
Read data 1
Registers
Read
register 2
Write
register
RegWrite
Write
data
Read data 2
UAL
ALUOp
I[15-11]
I[25-21]
I[20-16]
Read address
Instruction [31-0]
Instruction
memory
0mux1
RegDst
sign
extend
Read address
Read data
Data
memory
Write address
Write data
MemWrite
MemRead
MemToReg
1mux0
1mux0
ALUSrc
I[15-0]
Décodage de l’instruction ( Instruction Decode – ID )
Notes: Chemin de l’instruction est dirigé par des lignes de contrôle et de commande

## Slide 28: Etapes d’exécution d’une instruction MIPS
Read
register 1
Read data 1
Registers
Read
register 2
Write
register
RegWrite
Write
data
Read data 2
ALUOp
I[15-11]
I[25-21]
I[20-16]
Read address
Instruction [31-0]
Instruction
memory
0mux1
RegDst
sign
extend
Read address
Read data
Data
memory
Write address
Write data
MemWrite
MemRead
MemToReg
1mux0
ALUSrc
I[15-0]
Exécution de l’instruction ( EXecute – EX )
1mux0
UAL
Notes: Chemin de l’instruction est dirigé par des lignes de contrôle et de commande

## Slide 29: Etapes d’exécution d’une instruction MIPS
Read
register 1
Read data 1
Registers
Read
register 2
Write
register
RegWrite
Write
data
Read data 2
UAL
ALUOp
I[15-11]
I[25-21]
I[20-16]
Read address
Instruction [31-0]
Instruction
memory
0mux1
RegDst
sign
extend
Read address
Read data
Data
memory
Write address
Write data
MemWrite
MemRead
MemToReg
1mux0
1mux0
ALUSrc
I[15-0]
Accès à la mémoire des données ( Data Memory Access – MEM )
Notes: Chemin de l’instruction est dirigé par des lignes de contrôle et de commande

## Slide 30: Etapes d’exécution d’une instruction MIPS
Read
register 1
Read data 1
Registers
Read
register 2
Write
register
RegWrite
Write
data
Read data 2
UAL
ALUOp
I[15-11]
I[25-21]
I[20-16]
Read address
Instruction [31-0]
Instruction
memory
0mux1
RegDst
sign
extend
Read address
Read data
Data
memory
Write address
Write data
MemWrite
MemRead
MemToReg
1mux0
1mux0
ALUSrc
I[15-0]
Sauvegarde dans un registre ( Write back data – WB )
Notes: Chemin de l’instruction est dirigé par des lignes de contrôle et de commande

## Slide 31: Etapes d’exécution d’une instruction MIPS
Read
register 1
Read data 1
Registers
Read
register 2
Write
register
RegWrite
Write
data
Read data 2
UAL
ALUOp
I[15-11]
I[25-21]
I[20-16]
Read address
Instruction [31-0]
Instruction
memory
0mux1
RegDst
sign
extend
Read address
Read data
Data
memory
Write address
Write data
MemWrite
MemRead
MemToReg
1mux0
1mux0
ALUSrc
I[15-0]
Recherche (IF)
Décodage (ID)
Exécution (EX)
Accès Mem. (MEM)
(WB)
Notes: Chemin de l’instruction est dirigé par des lignes de contrôle et de commande

## Slide 32: Etapes d’exécution d’une instruction MIPS
Pas toutes les étapes sont nécessaires/obligatoires pour exécuter chaque instruction MIPS
A droite, un tableau illustrant les étapes requises pour notre exemple d’instructions
Instruction | Étapes requises |  |  |  | 
beq | IF | ID | EX |  | 
R-type | IF | ID | EX |  | WB
addi | IF | ID | EX |  | WB
sw | IF | ID | EX | MEM | 
lw | IF | ID | EX | MEM | WB